## Slide 1
CardioNet
Deep Learning for Cardiovascular Disease
Detection from 12-Lead ECG Signals
Hack4Health AI Challenge
Lower Division Submission
Brandon Whitehead

## Slide 2
The Problem
17.9M
deaths per year from
cardiovascular disease
The #1 cause of death globally
ECGs are cheap and ubiquitous, but
interpretation requires trained cardiologists
In rural and low-resource settings,
cardiologist access is severely limited
Can deep learning read ECGs like a cardiologist?

## Slide 3
Our Approach
Unique Dataset
PTB-XL: 21,799 clinical
12-lead ECG recordings
from PhysioNet
Deep Learning
1D ResNet with
Squeeze-and-Excitation
channel attention
Explainability
1D Grad-CAM heatmaps
show which parts of
the heartbeat matter
Most teams use tabular CSVs. We work with raw biomedical signals.

## Slide 4
The Dataset: PTB-XL
21,799
ECG Recordings
12
Standard Leads
10 sec
Per Recording
5
Diagnostic Classes
Task Framing: Binary Classification
Normal (NORM)
vs.
CVD Abnormality (MI, STTC, CD, HYP)
Ethically sourced, de-identified, freely available from PhysioNet.
Pre-defined stratified folds for reproducible evaluation.

## Slide 5
Model Architecture
CardioNet: 1D ResNet + Squeeze-and-Excitation Attention
12-Lead
ECG Input
(12 x 1000)
Stem
Conv
k=25, s=2
ResBlocks
x4 Stages
64-128-256-512
SE
Attention
Channel weights
GAP +
Classifier
Dropout + FC
Normal
vs CVD
Binary output
Residual Connections
Skip connections for stable training of deep networks
SE Channel Attention
Learns which feature channels (leads) matter most
18.7M Parameters
Trained end-to-end on a single T4 GPU in ~30 minutes

## Slide 6
Results
0.944
ROC-AUC
85.8%
Accuracy
0.860
F1 Score
What This Means
Strong discriminative ability between normal and CVD-affected ECGs.
High sensitivity to CVD cases -- better to flag a healthy patient for follow-up
than to miss a cardiovascular abnormality.

## Slide 7
Explainability: 1D Grad-CAM
Showing clinicians exactly what the model sees
How It Works
1. Compute gradients of the predicted class
score w.r.t. final conv layer activations
2. Global average pool gradients to get
per-channel importance weights
3. Weighted sum of activations + ReLU
produces temporal attention map
4. Interpolate and overlay on ECG waveform
as a color heatmap (yellow/red = high attention)
Clinical Relevance
ST-segment highlighting in ischemia cases aligns with cardiologist practice
QRS complex attention in conduction disturbance cases matches known physiology
Doctors can verify the model's reasoning before acting on predictions

## Slide 8
Translational Vision
From model to real-world impact
The Opportunity
Affordable ECG devices already exist for $30-80
(AliveCor KardiaMobile, etc.)
A compressed AI model on embedded hardware
could automate cardiac screening
Enables point-of-care screening in:
- Rural clinics
- Community pharmacies
- Developing nations
Deployment Path
Model quantization via TFLite/ONNX
for 4-10x size reduction
Target hardware: ESP32 or Raspberry Pi
for edge inference at the point of care
My embedded systems background
(ESP32, sensors, microcontrollers) makes
this a concrete next step, not a hypothetical

## Slide 9
CardioNet
Making cardiac screening accessible through AI
Thank you